Cookbook formulae for audio EQ biquad filter coefficients
---------------------------------------------------------
by Robert Bristow-Johnson, pbjrbj@viconet.com  a.k.a. robert@audioheads.com

All filter transfer functions were derived from analog prototypes (that
are shown below for each EQ filter type) and had been digitized using the
bilinear transform.  BLT frequency warping has been taken into account
for both significant frequency relocation and for bandwidth readjustment.

first, given a biquad transfer function defined as:

            b0 + b1*z^-1 + b2*z^-2 
    H(z) = ------------------------
            a0 + a1*z^-1 + a2*z^-2

this shows 6 coefficients instead of 5 so, depending on your architechture,
you will likely normalize a0 to be 1 and perhaps also b0 to 1 (and collect
that into an overall gain coefficient).  then your transfer function would
look like:

            (b0/a0) + (b1/a0)*z^-1 + (b2/a0)*z^-2
    H(z) = ---------------------------------------
               1 + (a1/a0)*z^-1 + (a2/a0)*z^-2

or

                      1 + (b1/b0)*z^-1 + (b2/b0)*z^-2
    H(z) = (b0/a0) * ---------------------------------
                      1 + (a1/a0)*z^-1 + (a2/a0)*z^-2


the most straight forward implementation would be the Direct I form (second equation):

   y[n] = (b0/a0)*x[n] + (b1/a0)*x[n-1] + (b2/a0)*x[n-2] - (a1/a0)*y[n-1] - (a2/a0)*y[n-2]

this is probably both the best and the easiest method to implement in the 56K.


now, given:

    frequency (wherever it's happenin', man.  "center" frequency or
        "corner" (-3 dB) frequency, or shelf midpoint frequency,
        depending on which filter type)
   
    dBgain (used only for peaking and shelving filters)

    bandwidth in octaves (between -3 dB frequencies for BPF and notch
        or between midpoint (dBgain/2) gain frequencies for peaking )

     _or_ Q (the EE kinda definition)

     _or_ S, a "shelf slope" parameter.  when S = 1, the shelf slope is
        as steep as you can get it and remain monotonically increasing
        or decreasing gain with frequency.
       

first compute a few intermediate variables:

    A     = sqrt[ 10^(dBgain/20) ]   = 10^(dBgain/40)    (for for peaking and shelving EQ filters only)
    omega = 2*PI*frequency/sample_rate
    sn    = sin(omega)
    cs    = cos(omega)
    alpha = sn/(2*Q)
          = sn*sinh[ ln(2)/2 * bandwidth * omega/sn ]     (if bandwidth is specified instead of Q)
    beta  = sqrt[ (A^2 + 1)/S - (A-1)^2 ]   (for shelving EQ filters only)

then compute the coefs for whichever filter type you want:

  the analog prototypes are shown for normalized frequency.
  the bilinear transform substitutes
 
                1          1 - z^-1
  s  <-  -------------- * ----------
          tan(omega/2)     1 + z^-1

LPF:            H(s) = 1 / (s^2 + s/Q + 1)

                b0 =  (1 - cs)/2
                b1 =   1 - cs
                b2 =  (1 - cs)/2
                a0 =   1 + alpha
                a1 =  -2*cs
                a2 =   1 - alpha

HPF:            H(s) = s^2 / (s^2 + s/Q + 1)

                b0 =  (1 + cs)/2
                b1 = -(1 + cs)
                b2 =  (1 + cs)/2
                a0 =   1 + alpha
                a1 =  -2*cs
                a2 =   1 - alpha

BPF:            H(s) = (s/Q) / (s^2 + s/Q + 1)

                b0 =   alpha
                b1 =   0
                b2 =  -alpha
                a0 =   1 + alpha
                a1 =  -2*cs
                a2 =   1 - alpha

notch:          H(s) = (s^2 + 1) / (s^2 + s/Q + 1)

                b0 =   1
                b1 =  -2*cs
                b2 =   1
                a0 =   1 + alpha
                a1 =  -2*cs
                a2 =   1 - alpha

peakingEQ:      H(s) = (s^2 + s*(A/Q) + 1) / (s^2 + s/(A*Q) + 1)

                b0 =   1 + alpha*A
                b1 =  -2*cs
                b2 =   1 - alpha*A
                a0 =   1 + alpha/A
                a1 =  -2*cs
                a2 =   1 - alpha/A

lowShelf:       H(s) = A * (A + beta*s + s^2) / (1 + beta*s + A*s^2)

                b0 =    A*[ (A+1) - (A-1)*cs + beta*sn ]
                b1 =  2*A*[ (A-1) - (A+1)*cs           ]
                b2 =    A*[ (A+1) - (A-1)*cs - beta*sn ]
                a0 =        (A+1) + (A-1)*cs + beta*sn
                a1 =   -2*[ (A-1) + (A+1)*cs           ]
                a2 =        (A+1) + (A-1)*cs - beta*sn

highShelf:      H(s) = A * (1 + beta*s + A*s^2) / (A + beta*s + s^2)

                b0 =    A*[ (A+1) + (A-1)*cs + beta*sn ]
                b1 = -2*A*[ (A-1) + (A+1)*cs           ]
                b2 =    A*[ (A+1) + (A-1)*cs - beta*sn ]
                a0 =        (A+1) - (A-1)*cs + beta*sn
                a1 =    2*[ (A-1) - (A+1)*cs           ]
                a2 =        (A+1) - (A-1)*cs - beta*sn